## Slide 1: Communication Counters, Timers and PWM
ECE433/ECC533

## Slide 2: What can you do with a counter?
Timer if source clock freq is know
Counter for events on input signal
  Start counting after an event
  Count edges of external signal
Generate output waveforms
  Frequency generator
  PWM
Capture time on an event
Generate a single pulse with programmable delay/width
Counter
Clk

## Slide 3: STM32L552 Timers
Types:
  SysTick (inside the CPU (Cortex-M33))
  General Purpose Timers
    Advanced (TIM1, TIM8)
    Standard (TIM2/3/4/5/15/16/17) and Basic (TIM6/7)
    Low-power Timer (LPTIMx)
From the datasheet

## Slide 4: SysTick
24-bit Count Down Timer embedded in the Cortex M33
Clock sources either CPU clock (1: HCLK) or 0: HCLK/8
When current counter value (VAL) transition to 0, VAL will be reloaded with LOAD. COUNTFLAG is asserted.
COUNTFLAG is cleared when it is read.
Registers are:
  SysTick->LOAD
  SysTick->CTRL
  SysTick->VAL
SysTick is defined in cortex_m33.h
#include "cortex_m33.h"
VAL
LOAD
COUNTFLAG=1
Time
LOAD
VAL (--)
CTRL
COUNTFLAG
==0
Reload
EN
CLKSOURCE
External Clk
System Clk

## Slide 5: Standard General-Purpose Timers
TIM2/5 are 32-bit
TIM3/4 are 16-bit
Modes:
  Input capture
  Output compare
  PWM generation (Edge- and Center-aligned modes)
  One-pulse mode output

## Slide 6: Timer Registers
TIMx->PSC : Clock prescaler, slows down source clock
TIMx->ARR : Auto Reload Reg, upper bound for counter
TIMx->CCMRn: Capture/Compare Mode Reg, operation mode
TIMx->CCER : Capture/Compare Enable Reg
TIMx->CCRn : Capture/Compare Reg, *action* when CNT==CCR
TIM2->CNT : Counter, real-time value of counter
TIM2->CRn : Control Reg, control for Timer IP

## Slide 7: 1- As a timer
#define COUNT_DW 0x10
RCC->APB1ENR1 |= 1; /* enable TIM2 clock */
TIM2->PSC = 160000 - 1; /* 16Mhz divided by 160000, 10ms per tick */
TIM2->ARR = 1000 - 1; /* divided by val */
TIM2->CNT = 0; /* clear timer counter */
TIM2->CR1 = 1|COUNT_DW; /* enable TIM2, start the counter 1, 2, 3 ... ARR-1 for COUNT UP */
CNT
ARR
UIF=1
Time

## Slide 8: 2- As a Counter Starting on ext. input signal
TIMx_ETR: An event (pos/neg edge) will cause timer to start counting.
// Start counting on posedge coming on PA0
RCC->AHB2ENR |= 1; //Enable GPIOA
GPIOA->MODER &= ~(0x3); // Clear the two bits for PA0
GPIOA->MODER |= (0x2); // Set the mode to AF (10--> 0x2)
GPIOA->AFR[0] &= ~(0xF); // Clear the 4 bits for PA0
GPIOA->AFR[0] |= (0xe); // Set the 4 bits to (AF14) to connect to TIM2_ETR
RCC->APB1ENR1 |= 1; /* enable TIM2 clock */
// Configure TIM2 to use external input as counter clock source
TIM2->SMCR = 0x0077; // Set Slave Mode Control Register with the following configuration:
// - External Clock Mode 1- Rising edges of the selected trigger (TRGI) clock the counter
// - External Trigger input (ETRF)
// - External trigger prescaler OFF
// - External clock mode 2 enabled.
TIM2->CNT = 0; /* clear counter */
TIM2->CR1 = 1; /* enable TIM2 to counts up */

## Slide 9: 2- As a Counter of ext. input signal
TIMx_IN: An event (pos/neg edge) will cause timer to increment by 1
// Configure LPTIM1 to use external input as counter clock source
// LPTIM_IN1b at PB5
RCC->APB1ENR1 |= 1 << 31; /* enable LPTIM1 clock */
LPTIM1->CFGR = 1|(1 << 23);/* use external clock source, increment counter using external input */
LPTIM1->CNT = 0; /* reset count to 0 */
LPTIM1->CR = 1; /* Enable timer */
LPTIM1->CR |= 0b101; /* Timer in continuous mode – LPTIM must be enabled */
LPTIM1->ARR = 100-1; /* count up 100 times */

## Slide 10: TIMx->CCMR
OCxM[3:0] configures the compare mode
  Set/clear/toggle on CCR match
  PWM

## Slide 11: 3- As Frequency Generator
// Using Toggle on match mode
RCC->APB1ENR1 |= 1; /* enable TIM2 clock */
TIM2->PSC = 16000 - 1; /* divided by 16000, for 1ms tick */
TIM2->ARR = 1000 - 1; /* divided by 1000 */
TIM2->CCMR1 = 0x30; /* set output to toggle on match */
TIM2->CCR1 = 400; /* set match value */
TIM2->CCER |= 1; /* enable CH1 compare mode */
TIM2->CNT = 0; /* clear counter */
TIM2->CR1 = 1; /* enable TIM2 */
CNT
ARR
UIF=1
Time
CCR1
Freq is controlled by ARR and PSC
Phase is controlled by CCR1

## Slide 12: Pulse Width Modulation
Pulse-width modulation (PWM), or pulse-duration modulation (PDM), is a method of reducing the average power delivered by an electrical signal, by effectively chopping it up into discrete parts. The average value of voltage (and current) fed to the load is controlled by turning the switch between supply and load on and off at a fast rate. (Wiki)

## Slide 13: 4- PWM - Edge aligned
// Use Case 2: PWM mode 1
RCC->APB1ENR1 |= 1; // enable TIM2 clock
TIM2->PSC = 16000 - 1; // divided by 16000
TIM2->ARR = 1000 - 1; // divided by 1000
TIM2->CCMR1 = 0x60; // PWM, High if CNT<CCR1 if count down
// or if CNT>CCR1 if count up
TIM2->CCR1 = 900; // set match value
TIM2->CCER |= 1; // enable CH1 compare mode
TIM2->CNT = 0; // clear counter
TIM2->CR1 = 0x11; // enable TIM2 , count down
CNT
ARR
UIF=1
Time
CCR1

## Slide 14: 5- PWM - Center aligned
// Use Case 3: PWM mode 1 - Center Aligned
RCC->APB1ENR1 |= 1; // enable TIM2 clock
TIM2->PSC = 16000 - 1; // divided by 16000
TIM2->ARR = 1000 - 1; // divided by 1000
TIM2->CCMR1 = 0x60; // PWM, High if CNT<CCR1 if count down
// or if CNT>CCR1 if count up
TIM2->CCR1 = 900; // set match value
TIM2->CCER |= 1; // enable CH1 compare mode
TIM2->CNT = 0; // clear counter
TIM2->CR1 = 0x61; // enable TIM2 , Center-aligned
CNT
ARR
UIF=1
Time
CCR1

## Slide 15: Basic Timers
TIM6/TIM7
16-bit count up
Overflow flag
Triggers the DAC

## Slide 16: Low-Power Timers
LPTIM1/2/3
16-bit count up
Can work in STOP mode with out LP clock running.

## Slide 17: Serial Port Plotter
Download the tool:
  https://github.com/CieNTi/serial_port_plotter/releases
Comprehensive Training:
  https://st-onlinetraining.s3.amazonaws.com/STM32L5-WDG_TIMERS-General_Purpose_Timer_GPTIM/index.html

## Slide 18: Reg Map:

## Slide 19: Reg Map: